## Slide 1: Saint2 Overview
David Anthony
david.c.anthony@aptiv.com

## Slide 2: Topics
Student Developers (only)
  TortoiseSVN
  Mantis
  FreeNAS \\10.207.142.31\Public
Wiki: http://sdt52.usinkok.northamerica.delphiauto.net/wiki/index.php/SAINT2
Overview
Saint2
  Bytes in a message
    Header Byte
      Header Byte Decode
    CAN ID
    Completion Code

## Slide 3: Topics (con’t)
  Time Stamp
  CAN Configuration
  Other busses
PC
  Saint Bus Engine (SBE)
  Saint Bus Monitor (SBM)
    Tx\Rx
    Periodics
    Emulation

## Slide 4: Topics (cont’d)
    Views
    .dbc file decode
  Make your own
    Visual Studio
      VB
      C++
      C#
    Excel

## Slide 5: Serial Bus Interface Tool – System Diagram
  Purpose: To provide an interface to a serial bus for a user, a test application, or another controller

## Slide 6: Serial Bus Interface Tool – General Features
User can interface with multiple buses concurrently with a single tool
Host interface is USB or RS232
The SAINT2 hardware is host and SD card configurable
The SAINT2 can be configured to send out periodic messages without a PC interface
The SAINT2 can be configured to act as a “gateway” between certain serial buses without a PC interface
The host can interface with discrete trigger out and trigger in pins

## Slide 7: Multiple Protocols
CAN (Block Transfer, ISO-15765-2)
  Single Wire
  Dual Wire
FT CAN
Class2 (J1850)
LIN
Keyword
SPI
IIC
Trig In\Trig Out

## Slide 8: Connections

## Slide 9: CAN features
CAN\CAN gateway
CAN\RS-232 Gateway
CAN listen only mode (No ACK)
Transceiver control
  Normal, Standby, Sleep, High Speed, High Voltage
ID filtering
  Reduce PC loading
Bus Flooding
ISO-15765-2 Transport protocol

## Slide 10: SAINT2 The SAINT2 Header Byte Format
SAINT2 Config Command | $08
IIC | $20 ($20 - $27)
KW2K | $28 ($28 – 2F)
CAN Node 1 | $50 ($50 - $57)
CAN Node 2 | $58 ($58 - $5F)
Class 2 | $60 ($60 - $67)
SPI | $78 ($78 – $7F)
LIN | $B8 ($B8 - $BF)
ISO15765-2 TP Node 1 | $C0 ($C0 – C7)
ISO15765-2 TP Node 2 | $C8 ($C8 – CF)
SAINT2 Protocol IDs
Bits 7 – 3 | Bit 2 | Bit 1 | Bit 0
Protocol ID | Command indicator bit | Tx/Rx indicator bit | Time Stamp Included bit
See Protocol ID table | =0: message is to be send or was received on the serial bus =1: message is a protocol related SAINT2 command or report | =0: message was received from the serial bus =1: message was transmitted by the S2 onto the serial bus | =0: the message does not contain a time stamp =1: a 2 byte time stamp is included in the message
SAINT2 Header Byte Format
$61 XX XX…  A Class 2 message received on the bus with a time stamp
$53 XX XX…  A CAN Node 1 message transmitted onto the serial bus with a time stamp
$5C XX XX…  A CAN Node 2 configuration command
Examples

## Slide 11: SAINT2 The SAINT2 Message Format
$51 07 DF 02 3E 80 00 00 00 00 00 10 23 67
SAINT2 Header
(CAN 1 RX msg)
Serial Message
($7DF 023E800000000000)
Completion Code
(Successful RX)
2 Byte Time Stamp
($2367)
SAINT2 Header
  indicates serial bus
  For Tx – must be pre-appended to the serial message by the user/plug-in
  For Rx – will be pre-appended to the serial message by the SAINT2 HW
Serial Message
  Actual serial message tx’d/rx’d on the serial bus
Completion Code
  A protocol specific byte indicating the success or error in the message tx or rx
  Appended to the serial message by the SAINT2 HW
  For CAN 0x08 successful Tx, 0x10 successful Rx
  Errors
Time Stamp
  2 bytes – 1ms/bit resolution
  Only included in the message if the SAINT2 header is odd
  Appended to the serial message by the SAINT2 HW

## Slide 12: 11-bit vs. 29-bit CAN messages
MSB of second byte set for 29-bit, off for 11-bit
  1st byte after header
11-bit
  000h-7FFh
  2 Bytes of ID
29-bit
  0000 0000h – 1FFF FFFFh
  4 Bytes of ID
Header | B2:b7-b3 | B2:b2-b0, B3 | Bytes 4-11
50/58 | 00000 | b10-b0 | D1-D8
Header | B2:b7-b5 | B2:b4-b0, B3, B4, B5 | Bytes 6-13
50/58 | 100 | b28-b0 | D1-D8

## Slide 13: SAINT2 How to TX/RX a Serial Message
Receive message is displayed as  $51 07 DF 02 3E 80 00 00 00 00 00 10 0A 32
SAINT2 Header
(CAN 1 TX msg)
Completion Code
(Successful RX)
2 Byte Time Stamp
($0A87)
Send Message Button
Enter Serial Message
Transmit message displayed
Receive message displayed
Transmit message is displayed as  $53 07 DF 02 3E 80 00 00 00 00 00 08 0A 87
User types in  $50 07 DF 02 3E 80 00 00 00 00 00
In this example: the CAN message is transmitted from PREPRO (CAN 1) and received on SZ00TL (CAN 1)
SAINT2 serial numbers
SAINT2 Header
(CAN 1 RX msg)
Completion Code
(Successful TX)
2 Byte Time Stamp
($0A32)
Enter SAINT2 Header
Same CAN message!
Why are the time stamps different?
The 2 SAINT2s don’t share a clock!

## Slide 14: SAINT2 Host Software SAINT Bus Engine 2 – A Closer Look
Plug-ins – select to execute an installed plug-in (must be installed in c:\program files\saint bus engine2\plugins)
Re-flash – select SAINT2 to launch the plug-in to reflash the SAINT2 firmware
Filters – set up filters to reduce number of messages passed to the plug-ins – good for busy buses or slow plug-ins (VB)
Device – Connected SAINT2 device. If it doesn’t show up here – make sure the correct USB driver is installed
Baud Rate – host interface baud rate NOT the serial bus baud rate – don’t bother to try to modify it – you can’t
Status – indicates if the device connection is open or closed – must be open to use – double click here to open or close the device
Bus Type – displays the SAINT2 firmware version running on the SAINT2
Don’t shut down the SBE2 – it must remain running!
If the SBE2 is running, restore its window using the icon in the system tray

## Slide 15: SAINT2 Configuring the SAINT2 box
How does the SAINT2 know what bus you want to send your message out on? What about the baud rate? What about the bus transceiver? 
THE SAINT2 MUST BE CONFIGURED!!
CAN Configuration
  Baud rate configuration
  Transceiver selection (Dual wire HS, SWCAN, FTCAN)
  Transceiver configuration (high speed, high voltage, normal, sleep…)
  Special protocol options (no ack error retries, listen only)
ISO15765-2 TP Configuration
  CAN IDs
  Frame padding
  Flow control options
Class 2 Configuration
  Normal vs. high speed
  Send break signal
KW2K
  Operating mode
  Baud rate
  Header and addressing configuration
  Initialization mode
  Protocol timing
  Etc…
LIN
  LIN version
  Baud rate
  Enable Automatic checksum generation
  Set up slave responses
SPI and IIC
  See SAINT2 Programmer’s Reference for caveats – these are not general purpose implementations

## Slide 16: SAINT2 The SAINT2 Header Byte
How do you indicate the serial bus you want your message transmitted on? How does the SAINT2 box indicate the serial bus it received a message on?
IT’S IN THE SAINT2 HEADER BYTE!!
Every transmitted and received message must have a SAINT2 header byte
The SAINT2 header byte indicates the message’s serial bus in b7 – b3
The SAINT2 header also indicates other useful information in b2 – b0
  Is the message a protocol configuration command or report?
  Was the message transmitted onto or received from the serial bus?
  Is there a timestamp included in the message?

## Slide 17: SAINT2 PC Software SAINT Bus Monitor 2
API
Custom User Apps
SAINT Bus Monitor 2
SAINT Bus Monitor 2
  Scrolling Message Monitor
  Transmit/Receive Messages
  Message Filtering
  Message Scripting
  Message Emulation
  Message Logging
  See SBM2 Help for more detail

## Slide 18: SAINT2 PC Software Custom User Plug-ins
API
Custom User Apps
Custom User Plug-ins
Plug-ins
  Custom – build it to do what you need it to do
  Development Environments supported
    VC++
    VC#
    VB / Excel VBA
  Templates\Instructions online
Custom User
Plug-in

## Slide 19: SBM Emulation
Automatically respond to incoming messages with either group file or single message
Simulate another product
WildCards – Just like Filters
  X – don’t care nibble
  x – don’t care bit

## Slide 20: SBM Group Files and Periodics
Group
Periodic
  Single
  Group

## Slide 21: SBM2 Color Filtering
Simply Double Click a message to assign

## Slide 22: SBM2 – Message File
List of often used messages entered in a text file (*.msg)
  Alleviates need to keep typing in the same messages
  Double Click to Send

## Slide 23: SBM2 – Misc
Send a message
Log Data
  Raw
  Decode (Protocol aware, ID, etc)
  Short
  ASCII
  WYSIWYG

## Slide 24: Visible Columns\WYSIWYG
Right Mouse Click on Columns (just like Outlook\Explorer)
Multiple Views at Once

## Slide 25: Saint2 LEDs

## Slide 26: Other
SBM Features to Demo
  Fixed Position Messaging
  .dbc file decoding
Not covered today
  CAN ISO-15765
  Stand-alone SD card configuration
  LIN, Keyword, SPI, IIC
  Gateway
  Reflash
  See Programmer’s Reference

## Slide 27: SAINT2 Special Features Embedded Periodic
Simple 08 90 message
  08 90 T1 T2 HH XX XX
Up to 16 embedded periodic messages (70-7F)
  Applications:
    Use for product keep alive
    Emulate “missing” bus nodes
  Advantages:
    Message periods are controlled by the SAINT2 firmware – no PC delays
    No PC needed – can also be configured with SD card/config.txt
    $08 73 00 07 D0 50 07 DF 02 3E 80 00 00 00 00 00  S2 will send a $7DF 023E800000000000 every 2 seconds
Configuration Command | Description
$08 7X 00 T1 T2 HH YY YY YY … | Turn periodic message 7X ON (X = 0 to F) T1 = MSB of 1ms/bit periodic time T2 = LSB of 1 ms/bit periodic time HH = SAINT2 Header (i.e. $60 for Class2, $50 for CAN) YY = Serial Message (1 to 15 bytes)
$08 7X 00 | Turn message 7X ON after it has already been configured
$08 7X 01 | Turn periodic message 7X OFF
$08 7X 10 | Delete periodic message 7X